## Slide 1: Agenda
Memory Exposure Reduction
  Process level (ASPLOS 2020)
  Intra-process level (ISCA 2020)
  Programming support (HPCA 2022)
Persistent Memory Defragmentation (ISCA 2022)
SoftPM: Software Persistent Memory (In submission)
SoC Contention Modeling (MICRO 2021)

## Slide 3: Memory Expousure Reduction Background
Memory
Dangling Pointer
Victim Data/Code
Prevent out-of-bound access
Reduced performance for normal execution
Memory attack
Limited programmability

## Slide 4: Memory Expousure Reduction Background
Trusted/Untrusted regions are identifiable
Solution: Permission control
Code A (trusted)
Code B (untrusted)
Code C (trusted)
Data A
Data B
Data C
Disable Data A and Data C permission
Enable Data A and Data C permission

## Slide 5: Memory Expousure Reduction Background
Trusted/Untrusted regions are unidentifiable
Solution: Principle of least privilege, reduce memory exposure
Code A
Code B
Code C
Data A
Data B
Data C
Enable Data B permission
Disable Data B permission
Enable Data A permission
Disable all data permission
Disable Data A permission
Disable Data C permission
Enable Data C permission

## Slide 6: Agenda
Memory Exposure Reduction
  Process level (ASPLOS 2020)
  Intra-process level (ISCA 2020)
  Programming support (HPCA 2022)
Persistent Memory Defragmentation (ISCA 2022)
SoftPM: Software Persistent Memory (In submission)
SoC Contention Modeling (MICRO 2021)

## Slide 7: MERR: Improving Security of Persistent Memory Objects via Efficient Memory Exposure Reduction and Randomization
Yuanchao Xu, Yan Solihin, Xipeng Shen
ASPLOS 2020
Notes: 1: I am Yuanchao Xu. I am from NC State University. I will introduce our work, called MERR: ~. This work is a collaboration with UCF.

## Slide 8: Security is more Important for PM
DRAM
Persistent Memory
Dangling Pointer
No System calls
Victim Data
Attacker
Users
Notes: 3: Security in the PM is more important. Without system calls protection, like open or close files. The attacker is able to use a dangling pointer to perform unauthorized reads and writes to the data. After they corrupted data, the corrupted data in the DRAM won’t be propagated to other processes beyond this process lifetime. However, the corrupted persistent memory data is able to propagate to other users beyond this process lifetime. To improve the security of persistent memory

## Slide 9: Idea: Memory Exposure Reduction & Randomization
Time
Program:
mmap (PM)
access PM
access PM
munmap (PM)
access PM
Memory Exposure
Attacker
Notes: We propose an idea:~
In the traditional program, the program will malloc the data and then perform acessess. After the last access, the program free the data. Between the malloc and free, the data is memory maped to this process. We regard this memory is exposed. This period time is memory exposure. The attacker is able to use the vulnerabilities to lauch attacks during the memory exposure. Our idea is to reduce the memory exposure into small temperature windows.

## Slide 10: Idea: Memory Exposure Reduction & Randomization
Time
Program:
mmap (PM)
access PM
access PM
munmap (PM)
access PM
Memory Exposure Reduction
Address Randomization
Info.
Attacker
Notes: The data is not mapped to a process out size these windows. Every time when we open the small temperature window, we also perform a runtime randomization. In this way, when the attackers try to launch software attacks outside the windeos, they will recive segement faults since the data is not mapped. Even though the attcker obtain some information, like memory layout, from a previous window. These infomation is useless in the next window due to runtime re-randomization.
Our method is not spefici to a perticular kind of attacks. We generally reduce vulbility to perform software memory discure and memory currption attacks. To efficently support this idea, we design MERR

## Slide 11: MERR
Architectural Support
MERR
Page Table Design
Time
Notes: It includes a simple but efficent page table design and a novel architecture support

## Slide 12: MERR
Architectural Support
MERR
Page Table Design
Time
70% Reduction 10% Overhead
80us Temporal Window
10^5 Randomization Frequency
Notes: The entire design is able to reduce 70% memory exposure rate with 10% overhead. Meanwhile, it provides a maximum 80us temporal window. At the same time, it provides 100 thougs randomization frequency with similar overhead compared to state-of-art heap data randomization work.

## Slide 13: Attach & Detach
PMO
Persistent Memory Object (PMO)
Physical Address Space
Attach
(PMO ID, Permission)
Process Address Space
PTEs
Detach(PMO ID)
Notes: One programming model of persistent memory uses attach and detach system calls. The persistent data is ognized as persistent memory objests in the physcial memory space. When an attach system call is invoked with PMO ID and permission. The process will initialied PETs that point to this PMO. The process can just use regular ld/st instructions to access this PMO. We assume the system has relocality support. This support can be either hardware or software. When a detach system call is invoked with PMO ID. This process will clean these PETs. Then, this data is removed from process address space. However, the overhead of attach/detach is not small.

## Slide 14: Efficiency Challenge
I GB PMO
Physical Address Space
Attach
(PMO ID, Permission)
Process Hierarchy Page Table
L3 Directory
L2 Directory
L1 Directory
PTE
PTE
PTE
PTE
PTE
262657 PTE Initiations!
PTE
PTE
PTE
PTE
…
…
Page Faults
PMO Access
Notes: Because current system use a hiereachy page table. For a 1GB PMO, when a attach system call is invoked, it needs to initalied 1 PTE in L3 dircotry, 512 PTEs in L2 dirctory, 200 thousand PTEs in L1 dirtory. There are 200 thousand PTE initilizations. The memory access to a recently-mapped PMO also incurs page faults. The challenge is how to support attach detach efficently.

## Slide 15: Embedding Page Table Subtree
I GB PMO
Physical Address Space
Process Hierarchy Page Table
L2 Directory
L1 Directory
PTE
PTE
PTE
PTE
PTE
PTE
PTE
PTE
…
…
L3 Directory
Notes: Our idea is embeding the page table subtree into PMO.

## Slide 16: Embedding Page Table Subtree
PTE
PTE
PTE
PTE
PTE
PTE
PTE
PTE
Data
Physical Address Space
Attach
(PMO ID, Permission)
Process Hierarchy Page Table
Metadata
Data
PTE
Detach (PMO ID)
Page Table Sub Tree
1GB PMO
One PTE Modification!
L3 Directory
Notes: This page table subtree is a part of metadata in the PMO. Now, when an attach system call is invoked for a 1GB PMO, the process only need to initlied one PTE. Then this PMO is mapped to this process. The process can use regular ld/st instruction to access entire PMO under the permission control. When an detach system call is invoed to this PMO. The process only need to clean one PTE to remove entire 1GB PMO from the process address space. This process is not able to access any data in this PMO. Whater how large the PMO is, both attach and detach system calls only need to modify one PTE.

## Slide 17: PMO Space Layout Randomization
PTE
PTE
PTE
PTE
PTE
PTE
PTE
PTE
Data
Physical Address Space
Attach
(PMO ID, Permission)
Process Hierarchy Page Table
Metadata
Data
PTE
Page Table Sub Tree
PTE
PTE
…
L3 Directory
1GB PMO
Notes: Based on this design, we are able to perform fast address space re-randomization. We call it PMO space layout randomization. For the attach system call, the random selector can select one of many possible PTEs. Then, it just intilied one PTE, the rerandomization is finished. For the relocatability support, perisistent memory programming model already has the relocalability support in software or hardware. we already have all reduction and randomization support. However, a new problem raises

## Slide 18: Permission Control Challenges
PTE
PTE
PTE
PTE
PTE
PTE
PTE
PTE
Data
Physical Address Space
Process Hierarchy Page Table
Metadata
Data
PTE
Page Table Sub Tree
Attach
(PMO ID, Permission)
L3 Directory
1GB PMO
Notes: The problem is permission control of PMO. When the process finishes the attach system call as previous steps.

## Slide 19: Permission Control Challenges
Data
Physical Address Space
Attach
(PMO ID, RW)
Process Hierarchy Page Table
PTE
PTE
PTE
PTE
PTE
PTE
PTE
PTE
PTE
…
…
Permission
Default
Permission
L3 Directory
1GB PMO
Notes: The requested read write permission is actually supported. In the current system, permission is per page permission which is checked in TLB. The permission is set and stored in the last level page table directory. We may use a default permission of this PMO. But when the requested permission is different from the default permission. All of last level PTEs need to be changed.

## Slide 20: Permission Control Challenges
Data
Physical Address Space
Attach
(PMO ID, RW)
Process 1 Hierarchy Page Table
L3 Directory
PTE
PTE
PTE
PTE
PTE
PTE
PTE
PTE
PTE
…
…
Different Permission
Process 2 Hierarchy Page Table
L3 Directory
PTE
Attach
(PMO ID, RO)
1GB PMO
Notes: Moreover, when a PMO is shared by two process with different permission, read write and read only. Only one embedded page table subtree cannot support this.

## Slide 21: Permission Matrix
ld/st instruction
TLB
Page-level Permission
Permission
Matrix
Process-wide PMO Permission
Most Strict Permission
Attach
Detach
Notes: Therefore, we propose an on-chip permission matrix per core to support Process wide PMO permissions in different processes. The basic idea is following, the ld/st instruction will use viritull address to check agained both TLB and permission matrix. Then, the process-wide PMO permission and page-level permission are obtained. After that, this access will check against most strict permission among these two to decide whether this access is legmaticl. Entires in the permission matrix are added by attach and entires are removed by detach.

## Slide 22: Hardware-Based Domain Virtualization for Intra-Process Isolation of Persistent Memory Objects
Yuanchao Xu, ChenCheng Ye, Yan Solihin, Xipeng Shen
ISCA 2020

## Slide 23: Security is more Important for PM
PMO1
Physical Address Space
Process Address Space
PTEs
PMO2
PTEs
Thread 1: Attach(PMO1, RW)
Thread 2: Attach(PMO2, RW)
Corruption is persistent!
Notes: title -> Here is an example
There are two PMOs in the PAS. Thread 1 invokes the attach system call to mmap PMO1 to the process address space.
Thread 2 from the same process also invokes the attach system calls to mmap PMO2 to the address space.
The thread 2 may use the bugs of the vulenrbility to currpt the data in PMO 2
After the termination of the process. The cupprted data is still there. The curroptin is persisetnt and it will be propogated to all future usage
We proposed to improve the security by using intra-process isoltaion

## Slide 24: Intra-process Isolation
Process Address Space
Domain 1
Domain 2
Data
Data
Set Permission
Unset Permission
Intentional or accidental access
Notes: intra-process isolation will saperate the process address space into several partions. In the example, we speart it into two parts.

## Slide 25: Intra-process Isolation for PM
Persistent Memory
PMO
Domain
(unique ID =PMO ID)
Intel Memory Protection Keys
16 protection keys
DomainsPKeys
Notes: each PMO => domain
PM => many domains
runtime time domain->pkeys

## Slide 26: Intra-process Isolation for PM
Persistent Memory
PMO
Domain
(unique ID =PMO ID)
Intel Memory Protection Keys
16 protection keys
DomainsPKeys
Application (process)
Client
Client
Client
Client
Client
Client
…
Hundreds of active domains
Notes: Howerever, server application
frequent remapping from domains to pkeys subsential overhead
two effcietn scalability problem

## Slide 27: Contribution
Domain Virtualization
MPK Virtualization
10X Software Virtualization
50X Software Virtualization
Intra-process Isolation for PM
Modest Aera Overhead

## Slide 28: Intel Memory Protection Keys (MPK)
Memory
Page 1
Page 2
Page 3
Page 4
PKey 1
PKey 1 Permission (--) | …
Thread 1 PKRU Register
Thread 1
WRPKRU (PKey 1, RW)
PKey 1 Permission (--) | …
Thread 2 PKRU Register
Notes: In memory. many pages
tag with pyhsical kesp
thread private PKRU register recordes the permission of pkeys
thread give

## Slide 29: Intel Memory Protection Keys (MPK)
Memory
Page 1
Page 2
Page 3
Page 4
PKey 1
PKey 1 Permission (RW) | …
WRPKRU (PKey 1, --)
PKey 1 Permission (--) | …
Thread 2 PKRU Register
Thread 1 PKRU Register
Thread 1
Min(Page permission, PKey permission)
Thread 2
Page permission ^ PKey permission
Notes: thread on access pages belong to pkeys 1
min page, pkey
success when minmum
when thred 2 wants
after access,

## Slide 30: Intel Memory Protection Keys (MPK)
Memory
Page 1
Page 2
Page 3
Page 4
PKey 1
PKey 1 Permission (--) | …
Thread 1
PKey 1 Permission (--) | …
Thread 2 PKRU Register
Thread 1 PKRU Register
Page permission ^ PKey permission

## Slide 31: Intel MPK Workflow
1
1
1
1
1
Page Table
Pkeys
PFN
NULL(0)
100
NULL(0)
101
NULL(0)
102
NULL(0)
103
NULL(0)
104
…
…
TLB
Access to 100
Pkeys
PFN
1
100
Pkey (1)
PKey 0 Perm. | PKey 1 Perm. | …
PKRU Register
Notes: More detal about MPK
to tag the memory pages, all of these pages for a domain need to be tagged
Then, when an access to one of these pages, TLB will load the PTE from page table with the pkey
after that, the pkyes is used to index the permission in PKRu register
acctually the second permission is the pkey 1 permission

## Slide 32: Inefficiency of Software Virtualization
1
1
1
1
1
Page Table
Pkeys
PFN
100
101
102
103
104
…
…
TLB
Pkeys
PFN
1
100
Pkey 0 Perm. | Pkey 1 Perm. | …
PKRU Register
PMO 1
PMO 2
1
103
1
1
1
1
1
Pkeys
PFN
200
201
202
203
204
…
…
NULL(0)
NULL(0)
NULL(0)
NULL(0)
NULL(0)
Clean Pkeys
NULL(0)
NULL(0)
NULL(0)
NULL(0)
NULL(0)
Set Pkeys
Store and restore permissions
PMO 1 Perm.
PMO 2 Perm.
TLB invalidations
All steps are needed when access evicted domain/PMO!
~4000 cycles, 1 eviction per 1000 instructions ~ 400% overhead
PMO 2 Perm.
Notes: The inef is f
when a PMO alraedy occupy the pkey and we wants to assing this pkey to another PMO.
we need to clcean ,set
permisison
TLB stores out

## Slide 33: Two Hardware Virtualization Design
Clean Pkeys
Set Pkeys
Store and restore permissions
TLB invalidations
MPK Virtualization

## Slide 34: Two Hardware Virtualization Design
Clean Pkeys
Set Pkeys
Store and restore permissions
TLB invalidations
Domain Virtualization

## Slide 35: Temporal Exposure Reduction Protection for Persistent Memory
Yuanchao Xu, Chencheng Ye, Yan Solihin, Xipeng Shen
HPCA 2022

## Slide 36
Process
PMO (Persistent memory objects)
Code A
Code B
Code C
(Buggy third parity libraries)
Attach (B, RW)
Detach (B)
Improving Security with Temporal Exposure
Expose the data to process/thread only when it needs to access the data
PMO
Physical Address Space
Process Address Space
PTEs
MERR [1]: attach and detach
Process-level map and ummap system calls for PM
Provide address randomization
[1] MERR: Improving Security of Persistent Memory Objects via Efficient Memory Exposure Reduction and Randomization, Xu et al. (ASPLOS 2020)
Access
Access
Access

## Slide 37
Thread
PMO (Persistent memory objects)
Code A
Code B
Code C
(Buggy third parity libraries)
WRPKRU(11)
WRPKRU(00)
Improving Security with Temporal Exposure
Expose the data to process/thread only when it needs to access the data
PMO
Physical Address Space
Process Address Space
(2) Intel Memory Protection Keys (MPK) [1]: WRPKRU
Thread-level permission control for memory domains
[1] https://www.kernel.org/doc/html/latest/core-api/protection-keys.html
Access
Access
Access
PTE 1
PTE 2
Domain
PTE 3
Permissions
\

## Slide 38
Adoption Challenge I: Lack of Composability
Thread 0
Thread 1
(1) Multithread composability
Attach (100, RW)
Detach (100)
Attach (100, RW)
Detach (100)
(2) Function composability for both
Error?
Silent?
Detach?
Thread 0
WRPKRU (1100)
WRPKRU (0000)
…
func ()
func () {
…
}
WRPKRU (1100)
WRPKRU (0000)
…
access
Disable
Error

## Slide 39
Adoption Challenge II: Three-way Tension
Security Goal: All Exposure Window (EW) is equal to or smaller than the target.
Programmability
Efficiency
Security Effectiveness
Granularity
if () {
for () {
…
}
if () {
…
}
else {
for ()
…
…
}
}
…
Attach ()
Coarse-grained Insertion
Fine-grained Insertion
Detach ()
Attach ()
Detach ()
Attach ()
Attach ()
Detach ()
Detach ()
Attach ()

## Slide 40: Contributions
Adoption Challenge I: Lack of Composability
Adoption Challenge II: Three-way Tension
EW-conscious Semantics
Compiler Support
Architecture Support to Combine EWs
Programmability
Efficiency
Effectiveness
TERP: Temporal Exposure Reduction Protection

## Slide 41: Overview of TERP
Programs with coarse-grained attach/detach
TERP Framework
Programs with coarse-grained attach/detach
Compiler Support
Programs with fine-grained attach/detach
Programmability
Architecture Support
Security
Efficiency & Security
Attach/Detach
System calls
Enable/Disable Permission (Intel MPK)

## Slide 42: Contributions
Adoption Challenge I: Lack of Composability
Adoption Challenge II: Three-way Tension
EW-conscious Semantics
Compiler Support
Architecture Support to Combine EWs
Programmability
Efficiency
Effectiveness
TERP: Temporal Exposure Reduction Protection

## Slide 43
EW-conscious semantics
Semantic Definition
Attach and detach may conditionally executed as thread permission enabling/disabling
No overlapped attach/detach in one thread
Allow temporal overlapped attach/detach from different threads
More detail in the paper about other semantic exploration and formulation
Thread 1
Thread 2
Thread 3
attach (A, R)
ld A
st A
detach (A)
attach (A, RW)
st A
detach (A)
ld A
Process Exposure window (EW)
Thread exposure window (TEW)
ld A
ld A

## Slide 44: Contributions
Adoption Challenge I: Lack of Composability
Adoption Challenge II: Three-way Tension
EW-conscious Semantics
Compiler Support
Architecture Support to Combine EWs
Programmability
Efficiency
Effectiveness
TERP: Temporal Exposure Reduction Protection

## Slide 45
Region 1
Compiler Support
Control flow graph
0
1
2
Basic blocks with PMO accesses
Basic blocks without PMO access
3
4
5
6
7
9
8
Path-sensitive insertion:
Each EW < Target
Attach ()
Detach ()
Detach ()
Attach ()
Control flow graph
Region analysis
Small regions: Direct insertion
Large regions:
Path-sensitive Insertion
Region 2
Detach ()
Direct insertion:
Longest execution path < Target
Attach ()

## Slide 46: Contributions
Adoption Challenge I: Lack of Composability
Adoption Challenge II: Three-way Tension
EW-conscious Semantics
Compiler Support
Architecture Support to Combine EWs
Programmability
Efficiency
Effectiveness
TERP: Temporal Exposure Reduction Protection

## Slide 47
attach (A)
detach(A)
Exposure Window Combining
Code is inserted with small EW (2us) security goal.
Dynamic combining to achieve the security goals
EW (randomization) (e.g., 40us)
TEW (permission) (e.g., 2us)
attach (A)
Computation
detach(A)
attach (A)
Computation
detach (A)
Target Exposure Window
attach (A)
Computation
detach (A)
Full Combining
Mis-combining
detach (A)
Long Computation
Target Exposure Window
Auto-detach (A)
Partial Combining
attach (A)
Computation
detach (A)
detach (A)
attach (A)
attach (A)
Target Exposure window
Randomize (A)
detach (A)
How to silent attach/detach?

## Slide 48
Architectural Support
PMOID | Time stamp (TS) | Counter of attached threads | Delayed detach (DD)
100 | 3 | 0 | 1
200 | 5 | 2 | 0
Circular Buffer
Attach (300, RW)
Cond_Attach
Attached?
Enable Perm.
Inc. Counter
Yes
No
Cond_Detach
Counter=0?
Disable Perm.
DD=1
Yes
No
Disable Perm.
Dec. Counter
T-TS<EW?
No
Detach
Yes

## Slide 49
attach (A)
detach(A)
Exposure Window Combining
Dynamic combining to achieve the security goals
Exposure window (randomization) (e.g., 40us)
Thread exposure window (permission) (e.g., 2us)
attach (A)
Computation
detach(A)
attach (A)
Computation
detach (A)
Target Exposure Window
attach (A)
Computation
Detach (A)
Full Combining
Mis-combining
detach (A)
Long Computation
Target Exposure Window
Auto-detach (A)
Partial Combining
attach (A)
Computation
detach (A)
detach (A)
attach (A)
attach (A)
Target Exposure window
Randomize (A)
detach (A)
How to auto-detach and randomization?

## Slide 50
Architectural Support
PMOID | Time stamp (TS) | Counter of attached threads | Delayed detach (DD)
100 | 3 | 0 | 1
200 | 5 | 2 | 0
Circular Buffer
Attach (300, RW)
Timer (T)
T-TopTS>EW
Randomization
Yes
counter>0
No
Detach()
Yes
Periodically Check

## Slide 51: Agenda
Memory Exposure Reduction
  Process level (ASPLOS 2020)
  Intra-process level (ISCA 2020)
  Programming support (HPCA 2022)
Persistent Memory Defragmentation (ISCA 2022)
SoftPM: Software Persistent Memory (In submission)
SoC Contention Modeling (MICRO 2021)

## Slide 52: FFCCD: Fence-Free Crash-Consistent Concurrent Defragmentation for Persistent Memory
Yuanchao Xu, Chencheng Ye, Yan Solihin, Xipeng Shen
ISCA 2022

## Slide 53
Persistent Fragmentation
Intel Persistent Memory
Higher Density
Byte-addressable Persistence
DRAM-like Performance
Persistent Memory Object Pool
Page 1
Page 2
Page 3
Page 4
Live object
First process
Second process
Third process
Persistent Fragmentation
Persistent fragmentation gets worsen with subsequent usages
Notes: object life time > process life time

## Slide 54
Performance Degradation from Persistent Fragmentation
Chart: Normalized Throughput (%)
| First Run | Second Run | Thrid Run | Fourth Run
2MB Page | 100 | 89.7 | 78.1 | 74.4
25% Reduction
Redis throughput for 2M insertions and 1M deletions
Notes: 美化图片

## Slide 55
Garbage Collection (GC)
Persistent Memory Object Pool
Page 1
1
Page 2
Live object
2
Pointer
Garbage Collection Steps
3) Compaction
Update Reference
GC metadata (forwarding table, etc.)
2: Not moved
3: Not moved
1) Marking
2) Summary
Relocation
2: Moved
Crash!
Inconsistent State!
Update metadata
2
How to design efficient crash-consistent GC?

## Slide 56
Concurrent Garbage Collection
Step 1: Marking
Step 2: Summary & Sweep
Step 3: Compaction
Relocation
Update reference
No Crash-consistent Requirement
Requires Crash-consistent Designs
CG Metadata
(e.g., compacting pages, forwarding table)

## Slide 57
Concurrent Compaction: Read Barrier
p->first = input //p points to object A
<read barrier>
1) Check A is in compacting page
2) Lookup new address
3) Check A is not moved
4) Memcpy A to the new address
    5) Update moved[A]=1
6) Update reference p to the new address
GC Metadata
(e.g., compacting pages, forwarding table)

## Slide 58
Crash-consistent Concurrent Compaction Baseline[1]
p->first = input //p points to object A
<read barrier>
1) Check A is in compacting page
2) Lookup new address
3) Check A is not moved
4) Memcpy A to the new address
    5) Update moved[A]=1
6) Update reference p to the new address
Persist GC metadata before compaction
(e.g., compacting pages, forwarding table)
sfence()
clwb(moved[A]);sfence()
[1] Mingyu Wu, et al. Espresso: brewing java for more non-volatility with non- volatile memory. ASPLOS 2018
Crash-consistency relocation incurs about 50% overhead!

## Slide 59
Can we remove the first sfence?
1 memcpy_nodrain(y,x,sizeof(A))
2 sfence();
3 moved[A]=1;
4 clwb(moved[A]);sfence();
5 o=y;
Observations
1) memcpy source data is clean
3) memcpy destination value is original or memcpy source
Post-crash inconsistent states
Compaction Page
Destination Page
Live object
Cacheline
GC metadata
moved[A]=1
2) References are not updated
Partially moved:
Single-fence solution
Recovery: compare values with memcpy source for objects without reference update
Differ: Redo memcpy and update moved
Same: Update moved
Notes: GC record this information

## Slide 60
Can we remove the second sfence?
1 memcpy_nodrain(y,x,sizeof(A))
2 moved[A]=1;
3 clwb(objA); sfence();
4 o=y;
Numerous possible post-crash inconsistent states
3) Memcpy destination value is original, memcpy source,
or the new value overwritten by application
Observations
1) memcpy source data is clean
If we can distinguish the original value from the new value
New value or memcpy source: Redo other cachelines of this object
Original value: Undo side effects
2) References may be updated

## Slide 61
Crash-consistent Concurrent Compaction Baseline
p->first = input //p points to object A
<read barrier>
1) Check A is in compacting page
2) Lookup new address
3) Check A is not moved
4) Memcpy A to the new address
    5) Update moved[A]=1
6) Update reference p to the new address
sfence()
clwb(moved[A]);sfence()
Fence-free design
More details in the paper

## Slide 62
Design Summary

## Slide 63
Design Summary

## Slide 64
Design Summary

## Slide 65: Agenda
Memory Exposure Reduction
  Process level (ASPLOS 2020)
  Intra-process level (ISCA 2020)
  Programming support (HPCA 2022)
Persistent Memory Defragmentation (ISCA 2022)
SoftPM: Software Persistent Memory (In submission)
SoC Contention Modeling (MICRO 2021)

## Slide 66: SoftPM: Software Persistent Memory
Yuanchao Xu, Wei Xu, Kimberly Keeton, David E. Culler

## Slide 67
Intel Optane DC Persistent memory
(Hardware Pmem)
HardPM hasn’t become ubiquitous in data centers
Another Way to Embrace Directly Addressable Persistence
Lower performance than DRAM
System software and application redesigns
System software and application optimizations
Battery rack
Data Center
Power
NV-DRAM
Directly addressable persistence
NV-DRAM has:
DRAM performance
Limited capacity *
Can NV-DRAM accelerate the adoption of HardPM?
Can NV-DRAM perform better than HardPM?
NV-DRAM (Software Pmem):
Conventional DRAM (DDR4) with rack-scale battery backup
Notes: By NV-DRAM we mean conventional large DRAM (DDR4, etc) with typically rack-scale battery backup …
* Explain on next slide

## Slide 68
NV-DRAM Limitation: Bounded Save Window
Battery
DRAM
Power
NV-DRAM
~60s data flush @ ~1GB/s
Storage
Save Window Size ~= Flush_time * Storage_BW
Persistent Region
Notes: Can’t flush everything in the persistent region.

## Slide 69
Applications are Architected with Persistence Models
Application
Data region
Log region
Necessary for
persistence
Storage
Old version of data region
Logs
Flush
Old version
Replay
Notes: Applications have utilized persistence for decades.
Typically transactional semantics require a log of some, in addition to the primary data object
Normal operations are performed both on the objects and the logs.
Log is periodically flushed to storage
Under failure, the in-memory object is restored from the old version, potentially, a snapshot.
The logs are replayed to restore it to a newer version

## Slide 70
SoftPM system
Software Persistent Memory Methodology
NV-DRAM
Storage
Applications
Dominate Persistence Models
Interfaces
Notes: %In general, HardPM presupposes a particular persistence model (what we call “large in-memory persistence”)
%SoftPM is flexible, as it is built from conventional, general purpose hardware
So the methodology of investigating it is important.
It has two aspects:
Identify the dominant persistence models used in applications
Structure the systems infrastructure accordingly
We walk through that in this talk
We focus on the performance under normal operation, restoration on failure is essentially the same as in conventional scenarios (such as persist to SSD or remote device)

## Slide 71: Agenda
Motivation
Application persistence models
SoftPM design and implementation
Multiple versions of Redis
Evaluation

## Slide 72
Persistence Models
Static:
Applications fully manage the fixed-size region
Append-only:
Applications consistently append logs to the in-memory region
Large in-memory persistence:
Data flushed from cache to memory is persistent
(a) Static
(b) Append-only
(c) Large in-memory
Notes: Structure the systems infrastructure accordingly

## Slide 73
SoftPM Static
Design
Tag all allocated regions as save window region

## Slide 74
SoftPM User-directed
Characteristics of append-only persistence model
Appended logs are not overwritten again
Design
Background flushing
Users can deliver read-only hints to the SoftPM system
Save window size control

## Slide 75
SoftPM Transparent
Design
Dirtiness-aware save window size control
User-transparent background flushing

## Slide 76
SoftPM Transparent Implementation
SoftPM pages are
write-protected
Write
Custom page fault handler
Dirty_pages = save_window?
Wait for finishing one page flush
Yes
No
1) Unset write-protected bit
2) Add this dirty page
Dirty page manager
Scan, clean and record all dirty pages’ reference bit
Periodically
Dirty pages> threashold
1) Flush LRU pages until dirty pages is smaller than the threshold
2) Set write-protected bit for flushed pages
Trap
Trigger

## Slide 77
(b) SoftPM User-directed
Multiple Versions of Redis
(a) Baseline

## Slide 78
(b) SoftPM User-directed
Multiple Versions of Redis
(a) Baseline

## Slide 79
Multiple Versions of Redis
(c) HardPM
(d) Hybrid
(e) SoftPM Transparent

## Slide 80
Summary of Multiple Versions of Redis

## Slide 81
Evaluation
Experiment setup
28-core Intel Xeon Platinum 8273CL@2.20GHz
6-channel HardPM, 6-channel DRAM and a SSD
All server and client threads are running on different cores in one socket
Unlimited save window size
Microbenchmark
YCSB
Limited save window size (30 GB SoftPM data, 3G (10%)-30G(100%) save window)
YCSB

## Slide 82
Microbenchmark Evaluation
SoftPM Transparent Improves 7%-88% throughput over the Hybrid

## Slide 83
YCSB Evaluation
SoftPM Transparent Improves 38%-93% throughput over the Hybrid

## Slide 84
YCSB Evaluation with Limited Save window
SoftPM incurs at most 9% overhead with 10% save window size

## Slide 85
Conclusion
SoftPM is potentially available using technology already provisioned in data centers today
SoftPM improves 38%-93% throughput over the well-optimized Hybrid (DRAM and HardPM) versions.
  Real DRAM performance memory
  Background flushing
  Cleaner designs
SoftPM also sets the performance bar that future HardPM and its ecosystem will need to beat.

## Slide 86: Agenda
Memory Exposure Reduction
  Process level (ASPLOS 2020)
  Intra-process level (ISCA 2020)
  Programming support (HPCA 2022)
Persistent Memory Defragmentation (ISCA 2022)
SoftPM: Software Persistent Memory (In submission)
SoC Contention Modeling (MICRO 2021)

## Slide 87: PCCS: Processor-Centric Contention Slowdown Model for Heterogeneous System-on-Chips
Yuanchao Xu, Mehmet E. Belviranli, Xipeng Shen, Jeffrey Vetter
MICRO 2021

## Slide 88: Heterogenous System-on-Chips (SoCs)
Smartphones
Autonomous Vehicles
Drones
Robots

## Slide 89: Diversely Heterogeneous Architectures
Chart: Number of Specialized IPs
| A4 (2010) | A5 (2011) | A6 (2012) | A7 (2013) | A8 (2014) | A9 (2015) | A10 (2016) | A11 (2017)
Number of Pus | 9 | 12 | 17 | 22 | 29 | 31 | 36 | 41
Apple A11 die photo
More than 40 intellectual property (IP) blocks in A11!
Source: http://vlsiarch.eecs.harvard.edu/research/accelerators/die-photo-analysis/

## Slide 90: Heterogenous SoC Example
Task 2
Task 3
Task 4
Task 6
Task 5
Task 1
Application
5-processor unit (PU) NVIDIA Jetson Xavier

## Slide 91: Heterogenous SoC Example
Task 1
Application
Task 2
Task 3
Task 4
Task 6
Task 5
5-processor unit (PU) NVIDIA Jetson Xavier

## Slide 92: Commercial SoCs are Challenge To Design
Which PUs to use?
# of Cores of PUs?
Frequencies of PUs?
Total bandwidth?
Performance Requirements
Budget
Constraints
Set of PUs
Target
Applications
Memory Contention
Analysis Memory Contention
Capture Contention effects
Predict co-located slowdown
Our work
Numerous possible designs
Several efficient designs

## Slide 93: Contributions
Built the fundamental understanding of memory contention on SoCs
Designed processor-centric contention-aware slowdown model
Identified the real bottleneck of SoCs at pre-silicon stage, saving up to 50% frequency or number of cores
Predicted accurate memory contention effects, improving
70% prediction accuracy over the state-of-the-art work

## Slide 94: Outline
Background
Observation
Architectural analysis
PCCS model
SoC design guidance

## Slide 95: Computer Architecture & Performance Models
Roofline Model
Performance model vs. Simulation
Source: https://commons.wikimedia.org/wiki/File:Example_of_a_naive_Roofline_model.svg
More insights
Less efforts and time
Don’t need architectural details
SoCs
Better utilization
Performance Models
Next generation SoCs
Gables
Our work
Post-silicon
Pre-silicon

## Slide 96: State-of-the-art Contention Model: Gables [1]
[1] Mark D. Hill, et al., Gables: A Roofline Model for Mobile SoCs, HPCA 2019
Roofline Model
PU 1
PU 2
PU 3
Memory Bandwidth Contention Model
Total BW demand < Peak BW
Total BW demand > Peak BW

## Slide 97: Something Gables Missing
Vary the task 1 BW demand
Task 1
PU 1 (GPU)
Task 2
PU 2 (CPU)
Vary the total external bandwidth demand from other tasks
Task 3
PU 3 (DLA)
Observe task 1’s performance:

## Slide 98: Observations
Vary the task 1 BW demand
Task 1 BW demand ≤ 30 GB/s
40 GB/s ≤ Task 1 BW demand ≤ 80 GB/s
Task 1 BW demand ≥ 80 GB/s
Task 1
PU 1 (GPU)
Task 2
PU 2 (CPU)
Vary the total external bandwidth demand from other tasks
Task 3
PU 3 (DLA)
Observe task 1’s performance:

## Slide 99: Outline
Background
Observation
Architectural analysis
PCCS model
SoC design guidance

## Slide 100: Architectural analysis
Hypothesis: Caused by fairness control in memory system

## Slide 101: Purpose of Fairness Control
Stream Access
Program
IP 1
Random Access
Program
IP 2
Memory 1
Memory 2
Thomas Moscibroda, et al., Memory Performance Attacks: Denial of memory service in multi-core systems, USENIX Security 2007

## Slide 102
Similar
Co-located
Performance
Stream Access
Program
IP 1
Random Access
Program
IP 2
Shared Memory
Significant
slowdown
Fairness control is important in memory controller
Reduce denial of memory service vulnerabilities
Improve overall throughput
Improve quality-of-service
Purpose of Fairness Control
Thomas Moscibroda, et al., Memory Performance Attacks: Denial of memory service in multi-core systems, USENIX Security 2007

## Slide 103: Bandwidth Partitions with Fairness Control
[1] Yoongu Kim, et al., ATLAS: A Scalable and High-Performance Scheduling Algorithm for Multiple Memory Controllers, HPCA 2010
ATLAS[1]: Similar attained service time
Peak BW 80GB/s
BW demands:
Obtained BW:
Stage 1
Stage 2
Stage 3
Task1: 60GB/s
Task2: 20GB/s
Task1: 60GB/s
Task2: 20GB/s
Stage 1
Stage 2
Task1: 60GB/s
Task2: 30GB/s
Task1: 50GB/s (83% of 60GB/s)
Task2: 30GB/s
Stage 3
Task1: 60GB/s
Task2: 80GB/s
Task1: 40GB/s (67% of 60GB/s)
Others: 40GB/s

## Slide 104
Methodology:
Memory Controller Policy Simulation
Task 1
Observe task 1’s
performance:
IP 1
Task 2
IP 2
Vary the total external bandwidth demand for other tasks
Task n
IP n
1
3
Vary task 1 bandwidth demands; Repeat Step 2
Implement memory controller policies in Ramulator[1]
2
[1] https://github.com/CMU-SAFARI/ramulator

## Slide 105
Memory Controller Policy Simulation
Name | Policies
FCFS | First-come-first-server.
FR-FCFS | First ready; First-come-first-server.
ATLAS | Higher the ranks of threads with least attained service.
TCM | Higher non-memory-intensive programs
SMS | Shortest first round robin
Close to Gables model
Close to the observations

## Slide 106: Outline
Background
Observation
Architectural analysis
PCCS model
SoC design guidance

## Slide 107: Processor-Centric Contention-aware Slowdown Model (PCCS)
Three-region interference-conscious Model
Piecewise slowdown functions in each region
Target PU’s Task BW demand
External BW demand
Achieved relative
speed under memory contention(%)

## Slide 108: PCCS parameters
Maximum Reduction of Minor Contention (MRMC)
MRMC
Total Bandwidth Demand with Contention (TBWDC)
TBWDC
Contention Balance Point (CBP)
CBP
Reduction Rate
Reduction Rate
More detail in the paper

## Slide 109: Outline
Background
Observation
Architectural analysis
PCCS model
SoC design guidance

## Slide 110
PCCS Model Usage
Task 1
IP 1
Task n
IP n
Task Placement Scheme
Standalone Performance
PCCS
BW
demands
Co-located
Slowdown
PU Variations
(#of cores, frequencies, features)
Memory Variations
(frequencies, # of channels, bit width)
Linear Scaling

## Slide 111: Case study
Objectives: Find appropriate frequencies of the GPU within 5% and 20% co-located slowdown on Xavier when external BW demands are 20GB/s, 40GB/s and 60GB/s
Program: streamcluster in Rodinia Benchmark Suite
Validation: Change the power settings of Xavier to obtain the ground truth
Methodology: PCCS model usage
Baseline: Gables model

## Slide 112: Results on streamcluster benchmark
Objective: within 5% slowdown
Objective: within 20% slowdown
External BW demand (GB/s) |  | 20 | 40 | 60 | Average | 20 | 40 | 60 | Average
 |  | Errors |  |  |  |  |  |  | 
 |  | PCCS |  |  |  | Gables |  |  | 
Maximum Allowed Slowdown | 5% | 2.4 | 3.1 | 1.6 | 2.4 | 4.8 | 35.4 | 41.9 | 27.4
 | 20% | 1.3 | 1.7 | 3.6 | 2.2 | 3.8 | 36.7 | 49.1 | 29.9

## Slide 113: Conclusion
Built the fundamental understanding of memory contention on SoCs
Predicted accurate memory contention effects, improving 70% prediction accuracy over the state-of-the-art work
Identified the real bottleneck of SoCs at pre-silicon stage, saving up to 50% frequency or number of cores
Designed three-region processor-centric contention-aware slowdown model
Thank you for your attentions!
Q & A