## Slide 1: Hardware-Based Domain Virtualization for Intra-Process Isolation of Persistent Memory Objects
Yuanchao Xu, ChenCheng Ye, Yan Solihin, Xipeng Shen

## Slide 2: Persistent Memory (PM)
Fast
DRAM
Disk
Persistent Memory
Non-volatile
Processor
ld/st Instructions
Persistent Data Structure
Notes: In the traditional memory hirachy. DRAM provide fast data access but the data in the dram is volital . Disk can keep data persistent but accesing Disk is slow.

## Slide 3: Attach & Detach Programing Model
PMO
Persistent Memory Object (PMO)
Physical Address Space
Attach
(PMO ID, Permission)
Process Address Space
PTEs
Detach(PMO ID)
Notes: The persisent memory is origninzed as PMOs. They are stored in the physical address space.
Attach system that mmap PMO to the process address space by initaliing PTEs. Process use ld /st
Detach

## Slide 4: Security is more Important for PM
PMO1
Physical Address Space
Process Address Space
PTEs
PMO2
PTEs
Thread 1: Attach(PMO1, RW)
Thread 2: Attach(PMO2, RW)
Corruption is persistent!
Notes: title -> Here is an example
There are two PMOs in the PAS. Thread 1 invokes the attach system call to mmap PMO1 to the process address space.
Thread 2 from the same process also invokes the attach system calls to mmap PMO2 to the address space.
The thread 2 may use the bugs of the vulenrbility to currpt the data in PMO 2
After the termination of the process. The cupprted data is still there. The curroptin is persisetnt and it will be propogated to all future usage
We proposed to improve the security by using intra-process isoltaion

## Slide 5: Intra-process Isolation
Process Address Space
Domain 1
Domain 2
Data
Data
Set Permission
Unset Permission
Intentional or accidental access
Notes: intra-process isolation will saperate the process address space into several partions. In the example, we speart it into two parts.

## Slide 6: Intra-process Isolation for PM
Persistent Memory
PMO
Domain
(unique ID =PMO ID)
Intel Memory Protection Keys
16 protection keys
DomainsPKeys
Notes: each PMO => domain
PM => many domains
runtime time domain->pkeys

## Slide 7: Intra-process Isolation for PM
Persistent Memory
PMO
Domain
(unique ID =PMO ID)
Intel Memory Protection Keys
16 protection keys
DomainsKeys
Application (process)
Client
Client
Client
Client
Client
Client
…
Hundreds of active domains
Notes: Howerever, server application
frequent remapping from domains to pkeys subsential overhead
two effcietn scalability problem

## Slide 8: Contribution
Domain Virtualization
MPK Virtualization
10X Software Virtualization
50X Software Virtualization
Intra-process Isolation for PM
Modest Aera Overhead

## Slide 9: Outline
Intel Memory Protection Keys (MPK)
Virtualization Analysis
MPK Virtualization
Domain Virtualization
Evaluation

## Slide 10: Intel Memory Protection Keys (MPK)
Memory
Page 1
Page 2
Page 3
Page 4
PKey 1
PKey 1 Permission (--) | …
Thread 1 PKRU Register
Thread 1
WRPKRU (PKey 1, RW)
PKey 1 Permission (--) | …
Thread 2 PKRU Register
Notes: In memory. many pages
tag with pyhsical kesp
thread private PKRU register recordes the permission of pkeys
thread give

## Slide 11: Intel Memory Protection Keys (MPK)
Memory
Page 1
Page 2
Page 3
Page 4
PKey 1
PKey 1 Permission (RW) | …
WRPKRU (PKey 1, --)
PKey 1 Permission (--) | …
Thread 2 PKRU Register
Thread 1 PKRU Register
Thread 1
Min(Page permission, PKey permission)
Thread 2
Page permission ^ PKey permission
Notes: thread on access pages belong to pkeys 1
min page, pkey
success when minmum
when thred 2 wants
after access,

## Slide 12: Intel Memory Protection Keys (MPK)
Memory
Page 1
Page 2
Page 3
Page 4
PKey 1
PKey 1 Permission (--) | …
Thread 1
PKey 1 Permission (--) | …
Thread 2 PKRU Register
Thread 1 PKRU Register
Page permission ^ PKey permission

## Slide 13: Intel MPK Workflow
1
1
1
1
1
Page Table
Pkeys
PFN
NULL(0)
100
NULL(0)
101
NULL(0)
102
NULL(0)
103
NULL(0)
104
…
…
TLB
Access to 100
Pkeys
PFN
1
100
Pkey (1)
PKey 0 Perm. | PKey 1 Perm. | …
PKRU Register
Notes: More detal about MPK
to tag the memory pages, all of these pages for a domain need to be tagged
Then, when an access to one of these pages, TLB will load the PTE from page table with the pkey
after that, the pkyes is used to index the permission in PKRu register
acctually the second permission is the pkey 1 permission

## Slide 14: Inefficiency of Software Virtualization
1
1
1
1
1
Page Table
Pkeys
PFN
100
101
102
103
104
…
…
TLB
Pkeys
PFN
1
100
Pkey 0 Perm. | Pkey 1 Perm. | …
PKRU Register
PMO 1
PMO 2
1
103
1
1
1
1
1
Pkeys
PFN
200
201
202
203
204
…
…
NULL(0)
NULL(0)
NULL(0)
NULL(0)
NULL(0)
Clean Pkeys
NULL(0)
NULL(0)
NULL(0)
NULL(0)
NULL(0)
Set Pkeys
Store and restore permissions
PMO 1 Perm.
PMO 2 Perm.
TLB invalidations
All steps are needed when access evicted domain/PMO!
~4000 cycles, 1 eviction per 1000 instructions ~ 400% overhead
PMO 2 Perm.
Notes: The inef is f
when a PMO alraedy occupy the pkey and we wants to assing this pkey to another PMO.
we need to clcean ,set
permisison
TLB stores out

## Slide 15: Two Hardware Virtualization Design
Clean Pkeys
Set Pkeys
Store and restore permissions
TLB invalidations
MPK Virtualization

## Slide 16: Two Hardware Virtualization Design
Clean Pkeys
Set Pkeys
Store and restore permissions
TLB invalidations
Domain Virtualization

## Slide 17: MPK Virtualization
TLB
PKRU Register
1
1
1
1
1
Page Table
Pkeys
PFN
100
101
102
103
104
…
…
PMO 1
PMO 2
1
1
1
1
1
Pkeys
PFN
200
201
202
203
204
…
…
NULL(0)
NULL(0)
NULL(0)
NULL(0)
NULL(0)
NULL(0)
NULL(0)
NULL(0)
NULL(0)
NULL(0)
PTE with PKey
PKey
Consecutive Virtual Address
…
…
Notes: basiclly need to clean and set pkeys to finish the remapping in page table level
consetive

## Slide 18: MPK Virtualization
NULL(0)
NULL(0)
NULL(0)
NULL(0)
NULL(0)
…
TLB
PKRU Register
1
1
1
1
1
Page Table
Pkeys
PFN
100
101
102
103
104
…
…
PMO 1
PMO 2
1
1
1
1
1
Pkeys
PFN
200
201
202
203
204
…
…
NULL(0)
NULL(0)
NULL(0)
NULL(0)
NULL(0)
PTE with PKey
PKey
Consecutive Virtual Address
…

## Slide 19: MPK Virtualization
1
1
1
1
1
Page Table
Pkeys
PFN
100
101
102
103
104
…
…
PMO 1
PMO 2
1
1
1
1
1
Pkeys
PFN
200
201
202
203
204
…
…
NULL(0)
NULL(0)
NULL(0)
NULL(0)
NULL(0)
Consecutive Virtual Address
1
1
1
1
1
200
201
202
203
204
…
…
Virtual Address Range
Pkey
TLB
PKRU Register
PTE with PKey
PKey

## Slide 20: MPK Virtualization
PMO 20
Access (VA)
Page Table
TLB
PKRU Register
TLB Miss
Store
Domain Translation TLB
VA Range
PKey
Perm.
PMO1 VA
1
RW
Notes: here is the work flow of our MPK virtulization design
Memory access to PMO 20, it carrys the virtual address.
When TLB miss, will chenge in parallel
in the domain tra..
then the evicted pkye is selected.
we need to store the permission from PKRU register to

## Slide 21: MPK Virtualization
PMO 20
Access (VA)
Page Table
TLB
PKRU Register
TLB Miss
Store
VA Range
PKey
Perm.
PMO1 VA
1
R-
Domain Translation Table
Writeback
Domain Translation TLB
Notes: write back the content of PMO 1 or domain 1 to the in memory table

## Slide 22: MPK Virtualization
PMO 20
Access (VA)
Page Table
TLB
PKRU Register
TLB Miss
VA Range
PKey
Perm.
PMO1 VA
1
R-
Domain Translation Table
Miss (VA)
Info.
Domain Translation TLB
Notes: after that the VA of PMO 20 access is used to obtain the imformation of PMO20.
these infor will update the entry to map the pkey 1 to domain 20

## Slide 23: MPK Virtualization
PMO 20
Access (VA)
Page Table
TLB
PKRU Register
TLB Miss
VA Range
PKey
Perm.
PMO20 VA
1
RW
Domain Translation Table
Domain Translation TLB

## Slide 24: MPK Virtualization
PMO 20
Access (VA)
Page Table
TLB
PKRU Register
Domain Translation Table
PKey
PTE
Pkey
PKey Permission
Update (PKey 1 Perm)
No extra runtime overhead
Fast permission changes
No system calls
Two entry updates
Programmer Transparent
VA Range
PKey
Perm.
PMO20 VA
1
RW
Domain Translation TLB
Notes: After that, the permission of domain 20 will update pkey 1 permission.
Then the pkeys 1 will added to PTE obtained from page table. The composed entry will be put into the TLB.
This the access will get the pkyes from TLB and use the PKyes to index the permission in PKRU register to get the pkeys permission.
All the logic of TLB hit doesn't change . For TLB hits it keeps the promissing feature provided by defualt MPK. no runtime overhead

## Slide 25: Second Hardware Virtualization Design
Clean Pkeys
Set Pkeys
Store and restore permissions
TLB invalidations
Domain Virtualization
Notes: I will introduce .
further TLB invalidations

## Slide 26: Inefficiency from TLB invalidations
TLB
PKRU Register
PKey
PKey 5 Perm
… | PMO X | …
Index represents PKey
… | PMO X | …
… | PMO X | …
…
Thread 0 PKRU register
Thread 1 PKRU register
Thread 20 PKRU register
Notes: before the inefficcy of TLB invalidation,
it is the logic
reasong
same mapping, index represent ID

## Slide 27: Inefficiency from TLB invalidations
TLB
PKRU Register
PKey
… | PMO Y | …
… | PMO X | …
… | PMO X | …
…
Thread 0 PKRU register
Thread 1 PKRU register
Thread 20 PKRU register
Thread 0 TLB
PMO X
PKey 5
TLB invalidation
PKey 5 Perm
Index represents PKey
Notes: when we mapping the pkey 5 from PMO X to PMO Y
The thread 0 holds the old mapping PMO

## Slide 28: Inefficiency from TLB invalidations
TLB
PKRU Register
Pkey
… | PMO Y | …
… | PMO Y | …
… | PMO Y | …
…
Thread 0 PKRU register
Thread 1 PKRU register
Thread 20 PKRU register
Thread 0 TLB
TLB invalidation
Thread 1 TLB
Thread 20 TLB
…
Buffer to replace Pkey mapping
PKey 5 Perm
Index represents PKey
Notes: And all threads holds the same mapping. TLB invalidations are needed for all threads TLBs
our idea is to use the buffer to repalce the key mapping to avoid TLB invalidations

## Slide 29: Domain Virtualization
PMO 20
Access (VA)
Page Table
Extend TLB
TLB Miss
Domain Table
VA Range
Domain ID
Notes: The work flow of domain virtuzation is following
for the PMO 20 access that carry the virtual address
TLB misses , till wil lchage both page table and domain table.
the domain table is used to obtain the domain id from the virtual address

## Slide 30: Domain Virtualization
PMO 20
Access (VA)
Page Table
Extend TLB
Permission TLB/Permission Table
PTE
Domain Table
VA Range
Domain ID
Domain ID
Domain ID
Domain Perm.
Domain ID
Permission
Not found  Inaccessible
Thread-private permission control
No TLB invalidation
Fast permission grant/change/removal
Notes: After that the PTE will add the domain ID and the new PTE will be put into exnted TLB.
Then the access will obtain the domain ID from TLB. the domain ID is ued to check the permission TLB and tnres are backedup with a in memory permission table
e permission TLB will give the permission from the domain ID and not found domain ID will be repated as inaccessble
After that, the domain permission is obtained

## Slide 31: Evaluation Methodology
Workloads:
  WHISPER benchmarks for 1 PMO
  Microbenchmarks with multiple PMOs
Architectural Overhead:
  Sniper Simulator (details in the paper)
Access pattern of multiple PMOs
  Randomly choose a PMO ID to access

## Slide 32: Performance
Microbenchmarks for multiple PMOs
10X Speedup
TLB Invalidation
50X Speedup
Cross-point for 16 entries
More results & analysis
in the paper
6X Speedup
Notes: I will present microbenchmark resuts. eans the number of active PMOs
yxais is the ovehread compared to no protection program.
ideal vritual means we assume there is no overhead of the virtulzation, it is the unrealict lower bound of the virtulization
Then the dot line is soft. subsitencail for 32 PMOs
the dash line is the hardw MPK virtlza

## Slide 33: Conclusion
Uncovered scalability limitations of software MPK virtualization for PMOs
Proposed protecting PMO by using intra-process isolation
Designed the hardware MPK virtualization that builds on top of MPK, achieving 10X speedup for 1024 domains
Designed the domain virtualization that achieves 50X speedup for 1024 domains